## Slide 1: The RiffMaster Music Education and Simulation System
A Digital Guitar Instrument Controller with an Integrated Web Application
ICON College of Technology and Management / Falmouth University
Tivadar Debnar (17663)

## Slide 2: Presentation Aim
This Presentation is a Retrospective Break Down of a Complex Engineering Project. We are Discussing Only the Following Aspects:
Hardware and Software Design Decisions,
Major Development Challenges,
The End Product’s Key Features and Functionalities,
Suggestions for a Future Marketable Device.
Several Phases will be Omitted For Brevity!

## Slide 3: Introduction
What is the idea?
What would make the device an improvement over existing ones?
What are the essential units or components?
Open Source: others may contribute or develop independently.

## Slide 4: The Controller Device
Inspirations: Guitar Hero and MI Digital Guitar
What Needs to be Improved on them?
Two Main Components:
Fret:
  6 x 20 Finger Positions
  Users Can Improve their Skills:
    Real Positions of Notes
    Muscle Memory and Transferable Skills
    Chord Patterns
    Scale Progressions
Strum:
  6 Individual Switches

## Slide 5: The Software Solution
An Authentic Guitar Instrument Make Features Possible Like:
  Realistic Guitar Game,
  Jam Session for Unconstrained Free Practicing,
  Music Tab Studio: Users can Create and Publish Playable Content.

## Slide 6: Set Up Milestones
Bare Minimum (any fails, the project fail):
A Fret Input that Reads the Activated Finger Positions
Strumming Unit that Triggers Messaging Between Device and the Application
Lightweight Protocol for Communication
Dependent Milestones:
Produce Sounds
Studio for Editing the Tab Content
Note Track for the Guitar Game
Limited App Functionality Focusing Only on Target Features
Potential Risk: Early Milestones are Dependent on Each Other. Project may be Delayed or Result in Complete Failure!

## Slide 7: Designing the Controller Device
How to Read the Controllers State?
Problems to Solve:
  Simultaneous Fret and Strum Actions
  Multiple Finger Positions on Fretboard (Chords)
  Multiple Presses on a Fret String (Hammer)
The Different Behaviours of Inputs:
  Strum Activates on Release
  Fret Button Activates on Press
Number of Fret Buttons: 120
Strum String Switches: 6
Other I/O: LEDs, Toggles
Microcontroller Selection: PIN Number Requires Arduino Due or Mega

## Slide 8: Wiring the Fret Board
Possible Wiring Solutions:
Linear and Logarithmic Resistor Ladders,
Switch Matrices.
Why Keyboard Switch Matrix?
How Matrix Wiring Works?
Challenges:
  Masking and Ghosting,
  Debouncing:
    Hardware Debounce Mechanism
    Software Debounce Correction

## Slide 9: Fret Development Challenges
Failed First Wiring Attempts as Too Many Components Need to Fit on the Neck.
Resulting in Contact Failures:
  Soldering are mm-s apart from each other,
  Button legs need wire extension,
  Use of universal PCB-s instead of free wiring.
The number of soldering points is approx. 600!

## Slide 10: Design and Development: Create Guitar Neck
Design Goals:
Simple and serviceable,
Provides protection,
Provides a strong connection into body ,
As compact as possible.
Problems:
Universal width (unlike real instrument),
Thicker than the expected,
Possible weak point.

## Slide 11: Body Design
Design Goals
Strong connection points and supports (pegs, screws),
Realistic design (actual guitar shape – Gibson Les Pauls),
Leave space for a separate strum unit,
USB Connection,
Provides Electric Housing for MCU, LEDs and Toggles…
Challenges
Cutting arcs,
Bending Walls.
Possible Problems
Inaccuracies: parts won’t fit
Weak points in the structure

## Slide 12: Develop the Controller Body
Cut and Bend Side Walls
Failed Attempts (5):
Less Heat:
  Material Breaks
More Heat:
  Plastic Melts
  Plastic Deforms
Cutting Arcs
Failed Attempts (3):
Plastic Melts
Plastic Snaps
Major Cracks
The material is sturdy but difficult to work with.
Supporting Pegs
11 Support Nut Peg
5 Extra Wall Support
MCU Placement
Embedding Neck
Possible Breaking Point!
Wiring
Wire Rows
Wire Columns
LEDs and Toggle
USB Conversion

## Slide 13: Strum Unit Design Options
Possible Strum Design Options (Pros and Cons)
Simple tactile switches (primitive solution),
Vibration or pressure sensors,
Magnetic and optical sensors,
Guitar Hero strum switch,
Lever based string switches.
What are Lever Switches and their Mechanics?
Relatively “easy” to implement,
Adjustable tension,
One of the most authentic solution.
Drawbacks of Mechanical Solutions
Not amateur friendly (users needs fine tuning),
Vulnerability to physical impacts,
Digital solution, unlike sensors.

## Slide 14: Strum Unit Development
Design Decisions
The unit can be taken out of the guitar body
  It is serviceable,
  Testable as a standalone unit.
Tensions can be set by a pair of screws:
  Main screw applies string pressure,
  Supplementary screw tunes button pressure.

## Slide 15: Head Stock
Why do we need a head stock at all?
Initial test result:
Buttons with caps are clumsy,
User needs to apply a lot of pressure,
Locating finger positions is problematic.
What improvement head stock made possible?
Supports strings on the neck,
More authentic than plain switches,
Easier to find finger positions.

## Slide 16: Protocol Options
Information Needs to be Communicated
Console’s fret state changes,
Console’s strum unit actions.
Possible Solutions
MIDI/OSI: A Commercial Industry Standard for Music Devices, such as Digital Keyboards and Music Apps
  Ideal for a final commercial product,
  May be an overkill for the prototype (prototype does not produce sound),
  Problematic to implement within the given time frame.
Binary:
  Highly performant solution,
  Not easy to debug as it is not humanly readable.
Textual and Numerical Messaging:
  Easy to read and test,
  Can be customised to fit the scenario,
  Short messages,
  We can use the device as a keyboard,
  NOT a standard solution.

## Slide 17: Custom Numerical Protocol
Events
  STRUM Active: Pressure on string,
  STRUM Passive: String released,
  FRET Active: Position is pressed,
  FRET Passive: Position is released.
Fret Number
  STRUM: Default 0 for Strum Events,
  FRET: Signifies Fret Position
String Number:
  STRUM and FRET: Denotes the Activated String
Message is Sent as a Stream of Keypress Events and Can be Translated (Assembled) into Custom Made Events.
Separation of Concerns: Device is NOT responsible about implementation details. E.g.: Every state change is communicated, not only uppermost fret positions.

## Slide 18: Controller State Management
  State Changes are Detected by
  Storing state in a 2D array,
  Storing previous and current state,
  Default is 1 (pullup resistor),
  Comparing state in each MCU loop,
  State Changes Trigger Messaging
  Assemble a sequence of keypresses:
    Event (Negate!),
    Fret Location,
    Activated String.

## Slide 19: Debounce Control
Detect Debouncing
Measure the time from last change,
Store the elapsed time for each switch.
Fret and Strum Behaves Differently!
Frets
Fret Active: only valid activation if the last active status is over threshold time,
Fret Passive: same for deactivation.
Strums
Strum Active: restart timer if changes happen in the debounce time.
Strings have natural bouncing.

## Slide 20: Backend
  We Will Use NodeJS and Mongo with Mongoose,
  We Create RESTful APIs,
  Several API Endpoints to Cover a Range of Frontend Features.
  Users: to Register and Login,
  Profile: for User Info,
  Subscription and Email Confirm Endpoints,
  Tabs:
    Creating Tablature Content,
    Modifying Tabs,
    Loading Tabs for Editor and Game,
  Play Sessions:
    The Accuracy and Precision,
    Timestamp,
    Points.

## Slide 21: Modelling and Routing
There is No Physical Relation Like MySQL
Embedding: Store Info from the Referenced Object (Performance Over Memory)
Reference: Store Object Reference IDs (Memory Efficiency over Performance)
ID Referencing will be Used as the App Has Low Frequency of API Calls.

## Slide 22: Security: JWT and Bcrypt
Passwords are hashed using bcrypt:
Every API expects a JSON web token signature (apart from subscription).
When user logs in receives JWT signature, and each API call header must have the token.
Tokens are stored locally using browsers local storage and page specific global variables.

## Slide 23: Subscription
Initially the User Has No JWT Token, Any Request will Redirect to the Login Page, Where Users Can Also Subscribe.
After an Input Validation the Server Checks If User Exists with the User Name. If No User Found in the Database, the Page Redirects to the Profile Creation Page.

## Slide 24: Profile
Users Choose an Avatar and Fill Up Some Input Fields Regarding their Profile Information.

## Slide 25: Email Confirmation
After Successful Subscription a Confirmation Email is Sent to the Users Email. This is to Protect Against Littering our Database with Fake Registrations.
We Use NodeMailer to Send Confirmation Emails, and Environmental Variables to Protect the Mail Servers Information.
The API Confirm Endpoint Sets the Users Active Status to True, an.d Redirects to the Login Page

## Slide 26: Login
Users Can Now Login to the Web Application.
The App Compares the Hashed Password and If Correct, Sends Back a JWT.
This JWT will be Passed Around through the Pages and for Each API Call.

## Slide 27: Home Page
Main Menu Options,
Playlist Cards,
Profile Info,
Dark Theme,
Neumorphism.
By Signing Out the Token is Deleted from Local Storage and Global Variables, that Immediately Redirects to Login

## Slide 28: Chords
Users can check over 12 thousand Chord Versions,
Select a main key,
Set a base note,
Set chord type.
The Chord Lookup is Based on Object Hashing Rather than Array Lookup for Performance!
The Chord Cards are Dynamically Created on Each User Selection.

## Slide 29: Jam Session
Custom made event listeners,
Actions trigger guitar display and equaliser refresh,
Only the topmost fret positions are played,
We will use howler for audio,
Interval timers for animation.
Performance of Different Browsers
Chrome: No significant delay,
Firefox and Edge: min 200ms delay!

## Slide 30: Tablature Data Structure
One structure for every feature!
Notation:
[notes, start, duration, super-text],
Multiple notes with same start position are compressed.
Memory efficient.

## Slide 31: Displaying Tabs
Single or Multi Lines,
Header
  Title and Tempo,
  Current Location (Bar and Note),
  Function Buttons,
  Metronome.
Tab Sheet
  N Bars with 32 Notes on 6 String,
  Only 4/4 Tempo is Supported,
  Custom Made Duration Icons,
  No Note Connection Lines (Although Possible).
Play Buttons
  Play, Pause, Stop,
  Step Forward / Backward,
  Record,
  Repeat Loop (From / To).

## Slide 32: Tab Editing
Add Chord Name,
Set Fret Position for Each String,
Set Duration for the Note,
Insert or Delete Bars,
Move Notes.
Tabs May be Recorded by the Guitar Device and Played Back!

## Slide 33: Saving and Loading Tabs
Tabs are Saved as Strings (JSON Stringify),
Automatic Tempo Detection,
Private and Public Settings,
Difficulty Setting.
Saved Tabs May Be Loaded
Display:
Title and Artist
Public / Private
Difficulty
Timestamp

## Slide 34: Practice and Play
Similar Functionalities (No Saving For Practice),
Score versus Accuracy.
Note Track:
  Determine Start and End of Each Note,
  Transform Tab into a Track Map,
  Past Notes are Faded,
  Current Note Highlighted.
Guitar Neck:
  Display User Actions on Device.

## Slide 35: Finishing Steps
Create more sample songs,
Public tabs cards must be clickable.
Current Solution Goes to a Specified Tab: Metallica - Noting Else Matters.
User Acceptance Testing
  Would Provide Further Feedback,
  A More Substantial Data Base for Scores and Plays.
Score Ranking and Other Achievements are Only Passible Afterwards,
Deploy Backend on Cyclic (Chosen Host Provider for Node Applications),
Deploy Frontend on One.com (Personal Website).

## Slide 36: Improving the Prototype
The device neck is too wide to be comfortable and accurate.
Improvements:
  PCB printing,
  Getting rid of tactile switch caps,
  Using a new 3 layer fret design (button base, neck surface and strings).
  3D Printing.
Strum may use optical sensors (it would not help the strange sound strings generate on plucking),
Patenting
There is no current patent for such a device,
Documentation must be complete and detailed for patenting,
Collision issues without lawyers.

## Slide 37: A Commercial Application
This Product is Not Profitable as a Game!
But with the Combination of:
  Instrumental Experience
  Software Gaming
  Educative Entertainment
  Social Platforming
We may achieve a comprehensive entertainment system with high chance of profitability.
By Digitalising Guitar Instruments We Can:
  Mass Produce Guitar Songs
  Improve Current Music Education
  Connect Students and Tutors
  Create Social Communities like Bands
  Collaborate: Think of a Musical GIT Versioning System
  Online Competitions
  Publishing Music
  Create News Feeds and Messaging, Commenting, Liking, Voting etc…

## Slide 38: A Futuristic Vision of RiffMaster
Standard ML Opportunities
Suggesting tabs to play based on previous interactions (Views, Plays, Likes…),
Suggesting tutors based on location or musical level,
Connecting users based on taste of music or other interests,
Creating playlist recommendations like Spotify.
Advanced AI Features
Determine what patterns make a song successful,
Help compose songs by autocorrecting or suggesting changes,
Diagnose play sessions and find patterns in mistakes,
Suggest tabs, songs that improve a more targeted learning outcome,
Drastically improve speed of learning.
Thank You for Your Attention!